## Slide 1
Darsi · free to copy for your school · IF/THEN: rules that act · 1
IF/THEN: rules that act
IoT · Level 3 · Lesson 2

## Slide 2
Darsi · free to copy for your school · IF/THEN: rules that act · 2
Today we will
Write automation rules as IF condition THEN action, with sensible thresholds.
Use two thresholds so devices don't flicker, and make the system fail safe.
Test rules against a day of data and judge comfort against energy.

## Slide 3
Darsi · free to copy for your school · IF/THEN: rules that act · 3
Rules that act
IF a condition, THEN an action
Choose thresholds from logged data
Two thresholds stop flicker
When a sensor fails, fail safe

## Slide 4
Darsi · free to copy for your school · IF/THEN: rules that act · 4
Rule cards through a school day
Warm-up (5 min): When should our fan run? Collect rules.
Teach (8 min): IF/THEN, thresholds and the flicker problem.
Play the day (12 min): Read out readings; devices stand when on.
Fix it (10 min): Two thresholds, and a plan for a silent sensor.
Wrap-up (5 min): Write one rule for a real school device.
Before class, write a day of readings on the board or a chart (time, temperature, light, tank level), with a stretch that wobbles around 30 °C and one hour when the tank sensor is silent. Pupils act the devices: no mains appliances are switched in class.

## Slide 5
Darsi · free to copy for your school · IF/THEN: rules that act · 5
Let’s discuss
Which school device would you automate first, and why?
Who should choose the balance between comfort and electricity?
What should happen when a sensor goes silent at night?

## Slide 6
Darsi · free to copy for your school · IF/THEN: rules that act · 6
Exit ticket
Write a two-threshold rule for the tank pump, and say what it does if the sensor goes silent.