## Slide 1
Darsi · free to copy for your school · Power: batteries and the sun · 1
Power: batteries and the sun
IoT · Level 3 · Lesson 3

## Slide 2
Darsi · free to copy for your school · Power: batteries and the sun · 2
Today we will
Estimate battery life from capacity and average current.
Explain why sleeping and sending less often make a sensor last longer.
Size a small solar panel and battery for a sensor that runs all year.

## Slide 3
Darsi · free to copy for your school · Power: batteries and the sun · 3
Power for sensors
Hours = capacity (mAh) ÷ average current (mA)
Plan with 70 % of the label
Sending costs most: send less often
Solar: battery for cloudy days, panel 3 × daily use

## Slide 4
Darsi · free to copy for your school · Power: batteries and the sun · 4
Battery-life sums
Warm-up (5 min): The garden sensor that died in the holiday.
Teach (10 min): Capacity ÷ average current, with the 70 % rule.
Sums (12 min): Groups work out their sensor card's battery life.
Challenge (8 min): Change one thing to last a whole term.
Wrap-up (5 min): Size a battery and panel for cloudy days.
Prepare one sensor card per group and work the answers beforehand; a coin cell with Wi-Fi or LoRa makes a good trap card. Use batteries only, never mains. Never cut, crush or puncture lithium batteries; an adult can open an old solar garden light with a screwdriver to show the panel, battery and LED.

## Slide 5
Darsi · free to copy for your school · Power: batteries and the sun · 5
Let’s discuss
Which school sensor needs fresh data every minute, and which could report once an hour?
Where at school would a solar panel get full sun all year?
Who will clean the panel and check the battery each term?

## Slide 6
Darsi · free to copy for your school · Power: batteries and the sun · 6
Exit ticket
A sensor averages 2 mA on 2,500 mAh of batteries. Planning with 70 %, about how many days will it last?