## Slide 1
Darsi · free to copy for your school · Networks: getting the data home · 1
Networks: getting the data home
IoT · Level 3 · Lesson 4

## Slide 2
Darsi · free to copy for your school · Networks: getting the data home · 2
Today we will
Compare Bluetooth, Wi-Fi, mobile networks and LoRa by range, power, data and cost.
Choose a network for a school sensor from its distance, power and data needs.
Explain how gateways and relays (a mesh) carry messages beyond one radio's reach.

## Slide 3
Darsi · free to copy for your school · Networks: getting the data home · 3
Choosing a network
Ask: how far, what power, how much data, what cost?
Near: Bluetooth LE or Wi-Fi
Far: a mobile network or LoRa
Out of reach: a gateway and relays

## Slide 4
Darsi · free to copy for your school · Networks: getting the data home · 4
The playground radio game
Warm-up (5 min): The tank sensor nobody can hear.
Teach (8 min): Four questions and four radios.
Play (15 min): Pass notes hop by hop to the gateway.
Choose (8 min): Draw the school; choose a network for one sensor.
Wrap-up (4 min): What happens when a relay fails?
Choose a safe, open space and agree a signal to stop. Pupils walk, never run, and pass notes only. A pupil who can't move about easily can be the gateway.

## Slide 5
Darsi · free to copy for your school · Networks: getting the data home · 5
Let’s discuss
Which school sensor would you connect first, and how?
What happens to the data if the gateway loses power?
When would a memory card collected weekly be enough?

## Slide 6
Darsi · free to copy for your school · Networks: getting the data home · 6
Exit ticket
A soil sensor 2 km from school, on batteries, sends 10 bytes an hour. Which network, and why?