## Slide 1
Darsi · free to copy for your school · When should it switch? · 1
When should it switch?
IoT · Level 3 · Lesson 2

## Slide 2
Darsi · free to copy for your school · When should it switch? · 2
Today you will
Choose a threshold for a rule from real readings.
Explain false alarms and misses, and decide which costs more.
Use two thresholds so a device doesn't flick on and off.

## Slide 3
Darsi · free to copy for your school · When should it switch? · 3
Choosing the number
Choose from real readings
False alarm or miss: which costs more?
Too many false alarms: nobody listens
Two thresholds stop the flicker

## Slide 4
Darsi · free to copy for your school · When should it switch? · 4
Find the two thresholds
Choose a device that switches itself: a fridge or a heater.
Make a table: time on, time off.
Listen for an hour and fill in the table.
Work out how long it runs and how long it rests.
Decide: one threshold, or two?
Don't open any device, touch wiring or hot parts, or unplug anything: just listen and watch. Ask before you go into someone else's room.

## Slide 5
Darsi · free to copy for your school · When should it switch? · 5
Let’s discuss
Which alarm in your life cries wolf, and what number would you change?
When is a miss worse than a false alarm?
Why does a fridge run for minutes, not seconds?

## Slide 6
Darsi · free to copy for your school · When should it switch? · 6
Check yourself
Give one alarm where a miss costs more, and one where a false alarm costs more.