## Slide 1
Darsi · free to copy for your school · Power from batteries and the sun · 1
Power from batteries and the sun
IoT · Level 3 · Lesson 4

## Slide 2
Darsi · free to copy for your school · Power from batteries and the sun · 2
Today you will
Explain why a device's radio uses more battery than anything else.
Make a battery last longer by sleeping and sending less often.
Describe how a small solar panel keeps a sensor running.

## Slide 3
Darsi · free to copy for your school · Power from batteries and the sun · 3
Make it last
Hours = capacity ÷ average current
The radio is the hungriest part
Sleep most of the time; send less
Sun by day, battery by night

## Slide 4
Darsi · free to copy for your school · Power from batteries and the sun · 4
Battery sums
Find two or three mAh labels.
Plan with 70% of each label.
Work out the hours at 100 mA and at 10 mA.
Plan a garden sensor: what, how often, which radio.
Decide: does it need a solar panel?
Never open, crush, puncture or heat a battery, and never leave lithium batteries or power banks in hot sun. Keep button batteries away from small children.

## Slide 5
Darsi · free to copy for your school · Power from batteries and the sun · 5
Let’s discuss
Which data around you must be fresh every second, and which could wait an hour?
Where at your school would a solar-powered sensor be useful?
Why does a coin cell suit Bluetooth LE but not Wi-Fi?

## Slide 6
Darsi · free to copy for your school · Power from batteries and the sun · 6
Check yourself
A sensor sends every minute over Wi-Fi. Name two ways to make its battery last longer.